NETWORK WIZARDS WIZCONSOLE EXAMPLE CONFIGURATION FILE

   The following is an example WizConsole configuration file.  It is
configured for eight serial host lines (1-8), 2 additional serial lines
(9-10), and 1 parallel port (11) with a printer.  Host line 1 is logged to
serial line 9.  Host lines 2 and 3 are logged to the printer (11).  Host line
4 has output timestamping enabled.  Host lines 6 thru 8 are logged to a file.


; WizConsole configuration file
;   Comments start with a semicolon and go to end of line.

;Main Parameters
cursor underscore	       ;block or underscore
input-buffer-size 16           ;Kbytes (2-32)
log-file directory C:\wizcon output-buffer-size 4 stamp 221
screen-blank 15		       ;minutes
video auto                     ;auto, mono, color, bw

;define interfaces
interface serial four 1 5 00 2bf 2a0 2a8 2b0 2b8  ;ports 1-4
interface serial four 5 7 00 1bf 1a0 1a8 1b0 1b8  ;ports 5-8
interface serial standard 9 4 01 3f8              ;COM1
interface serial standard 10 3 01 2f8             ;COM2
interface parallel standard 11 378                ;LPT1
;interface parallel standard 11 3bc               ;LPT1 on monochrome card

;defaults for host lines (1 thru 8)
line 1 8
output-buffer-size 1           ;Kbytes
speed 9600                     ;110,300,1200,2400,4800,9600,19200,38400,57600
bits-per-character 7           ;7, 8
parity even                    ;none, odd, even, mark, space
stop-bits 1                    ;1, 2
backspace-sends delete	       ;backspace or delete
flow-control none              ;none, harware, software (in, out)
monitor-dsr on	               ;on, off
new-line-mode off	       ;on, off
output-notify beep underscore  ;beep and/or underscore, or none
scroll-memory-lines 350        ;lines (minimum of 24)
stamp 000		       ;no stamps
terminal vt220		       ;dumb, monitor, vt52, vt100, vt220, wyse50
tabs 9 17 25 33 41 49 57 65 73 ;initial tab stops
wrap on                        ;on, off

;now set parameter specific to each line
line 1
name pluto

line 2
name zep
terminal vt52
flow-control hardware

line 3
name sun
output-notify none

line 4
name gateway
terminal dumb
stamp 310

line 5
name fs1
flow-control software

line 6
name server
backspace-sends backspace
log-to-file

line 7
name cookie
bits-per-character 8
log-to-file
parity none

line 8
name slowpoke
log-to-file

;remote dialup line
line 9
remote
password foobar
speed 2400

;serial printer on this line
line 10
speed 2400
monitor-line 1

line 11
name Epson
printer
monitor-line 2 3
setup-string "\033x\000\033M"   ;draft mode, 12cpi
stamp 220			;timestamp the output
output-buffer-size 4		;Kbytes